## Slide 1: Plan for Today (AP Physics I)
Finish notes from yesterday
Lecture/Notes on Power
Homework due Monday

## Slide 2: Power and Cost of Energy

## Slide 3: Equations
P = E/t
So given
V = PE/q
I = q/t
R = V/I
Derive the power equation

## Slide 4: Equation
P = PE/t =
Pe/q * q/t
P = VI or IV (like the plant)

## Slide 5: What are the other 2 equations?
Hint:
V = IR

## Slide 6: Power Equations
P = (IR) * I
P = I2 * R
P = (V/R) * V
P = V2/R

## Slide 7: Check Units on Both

## Slide 8: Other Equation

## Slide 9: Example
An electric motor draws 11 A at a potential difference of 120 V. It has an efficiency of 30%. How long does it take to lift a 500 kg piano a distance of 10 m?

## Slide 10: Example
An electric motor draws 11 A at a potential difference of 120 V. It has an efficiency of 30%. How long does it take to lift a 500 kg piano a distance of 10 m?
  P = IV
  Efficiency = Pout/Pin
  Pout = Mechanical Power
  Pin = electrical power

## Slide 11: Example
An electric motor draws 11 A at a potential difference of 120 V. It has an efficiency of 30%. How long does it take to lift a 500 kg piano a distance of 10 m?
  P out – mechanical power
  P = PE/t = mgh/t

## Slide 12: Example
An electric motor draws 11 A at a potential difference of 120 V. It has an efficiency of 30%. How long does it take to lift a 500 kg piano a distance of 10 m?
  Pin = IV = 11 * 120 = 1320 W

## Slide 13: Example
An electric motor draws 11 A at a potential difference of 120 V. It has an efficiency of 30%. How long does it take to lift a 500 kg piano a distance of 10 m?
  Pout = efficiency * Pin
  = .3 * 1320
  = 396 W

## Slide 14: Example
An electric motor draws 11 A at a potential difference of 120 V. It has an efficiency of 30%. How long does it take to lift a 500 kg piano a distance of 10 m?
  Pin = mgh/t
  t = mgh/Pin
  t = 500 * 9.8 * 10/396
  = 123.7 s

## Slide 15
What happens to the energy not used to pick up the piano?
Heat
Motors are inefficient
That’s why they heat up

## Slide 16: Example
A resistor of 15 ohms has a potential difference drop of 3 V.
  Find the current
  Find the power

## Slide 17: Example
A resistor of 15 ohms has a potential difference drop of 3 V.
  Find the current
  Find the power

## Slide 18: Example
A resistor of 15 ohms has a potential difference drop of 3 V.
  Find the current
  Find the power

## Slide 19: Example
A resistor of 15 ohms has a potential difference drop of 3 V.
  Find the current
  Find the power

## Slide 20: Example
A resistor of 15 ohms has a potential difference drop of 3 V.
  Find the current
  Find the power

## Slide 21: Kilowatt Hours
What is a kilowatt hour?
How your parents pay for electricity
What are the units?
Energy
In joules

## Slide 22: Kilowatt hour to Joules
In joules
1 kWh =

## Slide 23: What this means
How many parents complain about the cost of electricity when you leave a light on?
How much money are you actually wasting?

## Slide 24: Left on Light Example
100 W bulb left on for 1 hour
Cost of electricity in St. Louis is about 7 cents per kWhr

## Slide 25: Left on Light Example
100 W bulb left on for 1 hour
Cost of electricity in St. Louis is about 7 cents per kWhr
Convert to kWh

## Slide 26: Left on Light Example
100 W bulb left on for 1 hour
Cost of electricity in St. Louis is about 7 cents per kWhr
Convert to kWh

## Slide 27: Left on Light Example
100 W bulb left on for 1 hour
Cost of electricity in St. Louis is about 7 cents per kWhr
Now what is the cost?

## Slide 28: What this means
Next time your parents complain, toss them a penny and tell them to keep the change

## Slide 29: Cost to light a classroom
How much does it cost to light this room each day?
  12 fixtures
  Each fixture has 4 40W bulbs
  They are on for about 9 hours each day

## Slide 30: Cost to light a classroom
How much does it cost to light this room each day?
  12 fixtures
  Each fixture has 4 40W bulbs
  They are on for about 9 hours each day

## Slide 31: Cost to light a classroom
How much does it cost to light this room each day?
  12 fixtures
  Each fixture has 4 40W bulbs
  They are on for about 9 hours each day

## Slide 32: Cost to light the school each year
Say there are 180 days of school
About 130 teachers (some rooms are smaller than ours, but we have halls and gym and commons, so this is an ok estimate)

## Slide 33: Cost to light the school each year
Say there are 180 days of school
About 130 teachers (some rooms are smaller than ours, but we have halls and gym and commons, so this is an ok estimate)
This is actually not a big expense in the budget

## Slide 34: Cost of Electricity
Lights not a big expense
Air Conditioning is a big cost item
Fans, computers, etc also cost more

## Slide 35: Electricity Scavenger Hunt
Will find items around your house to find the Watts.
By estimating the time it’s used per month, you can find how much it costs