## Slide 1: Plan for Today (AP Physics I)
Turn in homework, cost of electricity chart and conceptual review
Lecture/Notes on Resistors in Series and Parallel Circuits

## Slide 2: Review
Talked about capacitors in series and in parallel
  Series – all in a row/one loop
    Electricity has one path to follow
  Parallel – separate paths for electricity to follow
  Same idea for resistors in series and parallel

## Slide 3: Resistors in Series
What will be the same for resistors in series?
What will change?
Current through all resistors has to be the same
IB = I1= I2 = I3
Why is this true?

## Slide 4: Resistors in Series
Current will be the same because of the law of conservation of mass/charge
Electrons don’t die, have babies, go on vacation, etc.
This means there is one path for the electrons and current to go through - same

## Slide 5: Resistors in Series
What is different?
Voltage from the battery (energy) gets distributed across all resistors (just like before)
VB = V1+ V2 +V3

## Slide 6: Resistors in Series
VB = V1+ V2 +V3
and V = IR
So IeqReq = I1R1 + I2R2 + I3 R3
But IB = I1= I2 = I3
Req = R1+ R2 + R3
Remember for capacitors in Series
1/Ceq = 1/C1+ 1/C2 + 1/C3

## Slide 7: Resistors in Parallel
What’s the same?
What is different?
Voltage all the same
Current is different

## Slide 8: Resistors in Parallel
VB = V1= V2 =V3
IB = I1+ I2 + I3
Req = ?
What is your expectation?
1/Req = 1/R1+ 1/R2 + 1/R3

## Slide 9: Resistors in Parallel
IB = I1+ I2 + I3
I = V/R
VB/Req = V1/R1 + V2/R2 + V3/R3
Vs all same
1/Req = 1/R1+ 1/R2 + 1/R3

## Slide 10: Tool Kit
Series
VB = V1+ V2 +V3
IB = I1= I2 = I3
Req = R1+ R2 + R3
1/Ceq = 1/C1+ 1/C2 + 1/C3
Parallel
IB = I1+ I2 + I3
VB = V1= V2 =V3
1/Req = 1/R1+ 1/R2 + 1/R3
Ceq = C1+ C2 + C3

## Slide 11: Example
Suppose with have a 4 ohm, 7 ohm, and 12 ohm resistor connected with a 6V battery. Find I and V for series and parallel

## Slide 12: Series
Vs add
Is same
Rs add = 23
I = 6/23 = .26 A
V4 = 1.04
V7 = 1.83
V12 = 3.13

## Slide 13: Parallel
Vs same
Is add
V = 6
I4 = 1.5
I7 = .86
I12 = .5 A