## Slide 1: Plan for Today (AP Physics I)
Test review
Go over Conceptual Review Problems
Test Review problems

## Slide 2: Calculate current, number of electrons per unit of time, and rates of flow
I = Q/t
Q = I * t
Then convert to number of electrons
Rate of flow = current

## Slide 3: Apply Ohm’s law and know how to determine if a resistor follows Ohm’s law
Ohm’s Law -> V = IR
  Given 2, be able to calculate the 3rd
A resistor follows Ohm’s Law if its resistance stays constant as V and I increase
  If it does, it’s Ohmic, if it doesn’t, it’s non-ohmic

## Slide 4: Know and apply the factors that change the resistance of an object
Increase in temperature increases resistance
Increase in length increases resistance
Increase in cross-sectional area decreases resistance
Equations:
  R = p l/a
  Rf = Ro(1 + a(Tf – Ti))

## Slide 5: Calculate the cost of electricity
Cost – cents/kWh
Convert energy to kilowatt hours
  Power in watts – P = IV
  Watts to kilowatts
  Multiply answer by time in hours

## Slide 6: Apply Ohm’s law to simple series and parallel circuits and know the difference between a parallel and series circuit
Series
  Voltages add, Currents all same, Rs add
  Vb= V1 + V2 + V3
  Ib = I1 = I2 = I3
  Req = R1 + R2 + R3
Parallel
  Voltages all same, currents add, 1/Req adds
  Vb = V1 = V2 = V3
  Ib = I1 + I2 + I3
  1/Req = 1/R1 + 1/R2 + 1/R3
Series – one path for current to follow
Parallel – more than one closed path

## Slide 7: Collapse and analyze parallel, series, and complex circuits
Circle around – only one wire in and out
Use Ohm’s law and the previous rules to solve

## Slide 8: Example Problem - 1
When we cooked the pickle in class, we had it plugged in for 1.5 minutes. The pickle had a resistance of about 250 ohms and the outlet was 120 V.
  Find the current through the pickle
  The power used
  The total number of electrons that passed through the pickle

## Slide 9: Example Problem - 2
You leave a light on while you are away from school for 9 hours. The light bulb says it has a current of 2 A and it is plugged in to a 120 V outlet. If the cost of electricity is 8 cents/kWhr, how much money did you waste leaving the light on?

## Slide 10: Example Problem - 3
Draw a diagram of how a voltmeter and ammeter should be placed in a series circuit with two resistors to measure the voltage and current through one of the resistors.

## Slide 11: Example Problem - 4
A tungsten wire in a light bulb has a diameter of 1.2 mm. When turned on, the temperature increases from 20 C to 970 C. This wire is 1 cm long. What is the resistance of the tungsten at 970 C?

## Slide 12: Example Problem - 5
Describe how a dimmer switch in your house works

## Slide 13: Example Problem - 6
Given the following resistors, create 2 circuits – one that maximizes and the other that minimizes the current. Find the current in each.
  R1 = 6 ohms
  R2= 4 ohms
  R3 = 10 ohms
  Battery = 9 V

## Slide 14: Example Problem - 7
Explain how you can find the voltage, current, and resistance in a series and parallel circuit.

## Slide 15: Example Problem - 8
What happens to the total resistance when you add a resistor in series?
What happens to the total resistance when you add a resistor in parallel?

## Slide 16: Example Problem - 9
A 2 ohm, 3 ohm, and 4 ohm resistor are connected to a 9 V battery. Find the current and voltage for each resistor if they are
  Connected in series
  Connected in parallel

## Slide 17: Example Problem - 10
Write equations using Kirchhoff’s Rules to analyze the circuit.

## Slide 18: Example Problem - 11
Why does length effect the resistance of an object?

## Slide 19: Example Problem - 12
How can you tell if a material is nonohmic?

## Slide 20: Example Problem - 1
When we cooked the pickle in class, we had it plugged in for 1.5 minutes. The pickle had a resistance of about 250 ohms and the outlet was 120 V.
  Find the current through the pickle
  The power used
  The total number of electrons that passed through the pickle

## Slide 21: Example Problem - 2
You leave a light on while you are away from school for 9 hours. The light bulb says it has a current of 2 A and it is plugged in to a 120 V outlet. If the cost of electricity is 8 cents/kWhr, how much money did you waste leaving the light on?

## Slide 22: Example Problem - 3
Draw a diagram of how a voltmeter and ammeter should be placed in a series circuit with two resistors to measure the voltage and current through one of the resistors.

## Slide 23: Example Problem - 4
A tungsten wire in a light bulb has a diameter of 1.2 mm. When turned on, the temperature increases from 20 C to 970 C. This wire is 1 cm long. What is the resistance of the tungsten at 970 C?

## Slide 24: Example Problem - 5
Describe how a dimmer switch in your house works

## Slide 25: Example Problem - 6
Given the following resistors, create 2 circuits – one that maximizes and the other that minimizes the current. Find the current in each.
  R1 = 6 ohms
  R2= 4 ohms
  R3 = 10 ohms
  Battery = 9 V

## Slide 26: Example Problem - 7
Explain how you can find the voltage, current, and resistance in a series and parallel circuit.

## Slide 27: Example Problem - 8
What happens to the total resistance when you add a resistor in series?
What happens to the total resistance when you add a resistor in parallel?

## Slide 28: Example Problem - 9
A 2 ohm, 3 ohm, and 4 ohm resistor are connected to a 9 V battery. Find the current and voltage for each resistor if they are
  Connected in series
  Connected in parallel

## Slide 29: Example Problem - 10
Write equations using Kirchhoff’s Rules to analyze the circuit.

## Slide 30: Example Problem - 11
Why does length effect the resistance of an object?

## Slide 31: Example Problem - 12
How can you tell if a material is nonohmic?